## Slide 1: c3e, TU-Braunschweig
Rolf Meyer

## Slide 2: History of the Department

## Slide 3: SystemC/TLM
Wolfgang Klingauf
Greenbus
GSGP
TLM2
GreenSocs
Robert Günzel
OCP TLMKit
Carbon AmbaKit
Christian Schröder
GSParam
GreenAV
GreenControl
CCI

## Slide 4: Department change
Golze  Berekovic
Mathematics/Computer science  Electrical/computer engeneering .
Berekovic:
ESA
SMART
RECOMP
R3-Cop

## Slide 5: ESA ESTEC HW-SW-SIM  SystemC/TLM
A TLM Hardware Platform for space

## Slide 6: Overview Intended use of activity output
Enable ESA to develop new Virtual Platforms based on a set of key SystemC IP simulation models
Distribute platform and models to contractors without being subject to any fee or restrictions
Improve future SoC Design efficiency:
  Enable SW development before HW is ready
  Gradual system refinement from TLM to RTL
  Benefit from early architecture exploration
Productivity
Availability
Accessibility
Consistency
Advantages of virtual platforms
Notes: The motivation behind our project was …
to enable ESA to develop new Virtual Platforms based on a set of key SystemC IP simulation models
In order to be able, in the future, to distribute platform and models to contractors without being subject to any fee or restrictions
… and in general to improve SoC Design efficiency by extending the existing design methodology to system level
In particular by enabling SW development before HW is ready
Enable gradual System refinement from transaction level down to RTL
And to benefit from high-level architecture exploration

## Slide 7: Tools Platform utilizes GreenSoCs TLM infrastructure
Explored commercial and open-source Virtual Platform solutions.
Selected appropriate infrastructure components:
GreenReg
  Framework for SystemC register modeling
  Register bank container which can be bound to TLM sockets
  Bit-field callback functions etc.
AMBA Sockets
  TLM convenience sockets with build-in memory management
  Predefined payload extensions for modeling AMBA bus transfers
GreenControl
  Parameter API for model configuration
  Debugging, Tracing, runtime-reconfiguration
www.greensocs.com
Notes: As mentioned our first task was to look around and get an overview about what is on the market place in terms of virtual platform tools and infrastructure.
We have been looking at commercial tools, particularly the ones from Cadence and Synopsys, and open source solutions like SoCLib and Unisim.
I don’t want to go into depth here. The outcome was that we decided, together with ESA, to start with three open source SW packages from GreenSoCs.
GreenSocs is not a self-contained virtual platform like most of the other systems we looked at. It is more like an open platform for TLM infrastructure development.
Within GreenSocs there are different projects without strong dependency on each other. That basically means, you can pick what you like, without being imposed to undesired overhead.
We decided to use GreenReg, which is a framework for SystemC register modeling. It gives you register bank containers which can be bound to TLM sockets, bitfield read/write callbacks and so on.
Second, the GreenSocs AMBA Sockets. Those basically are TLM convenience sockets with build-in memory management and pre-defined payload extensions for modeling AMBA bus transfers.
And GreenControl. Greencontrol is a parameter API for model configuration, debugging and tracing.

## Slide 8: High-Level Modeling of SystemC IPs IPs modeled in course of project
Models provided by ESA (integration only)
Mandatory/Optional IPs
GPTimer
Models with GRLIB reference
AHB2SW
AHBCTRL
LEON ISS
mmu-cache
i/d cache mmu
localrams
MCTRL
SRAM
SDRAM
IO
PROM
SoCWire
GPTimer
SpaceWire
IRQMP
AHB2APB
AHBOUT
AHBIN
AHBMEM
APBUART
bus
masters
bus
slaves
AHBProf
Additionally/secondary models
All models available in loosely timed (LT), and approximately timed (AT) flavor of TLM2.0.
Notes: This is an overview about the SystemC/TLM models that have been built in the course of this project.
All models are available in loosely timed and approximately time flavor of TLM2.
The red boxes show preexisting models, the most important one the TrapGen LEON ISS from ESA.
The blue boxes are boxes show mandatory and optional components. Modeling these IPs was our main job.
- We have here a complex IP containing models for instruction and data cache, localrams and a sparc MMU.
An AHB bus with support for plug & play and snooping.
A memory controller with support for SRAM, SDRAM, IO and ROM; including a generic memory model
A timer and a multi-processor interrupt controller
To complete the system we provide some additional IP like an AHB2APB bridge, and AHB memory and an APB UART.
The AHBIN, AHBOUT and AHBProf components have no correspondence in the GRLIB, but have been proven useful for simulation control and testing.

## Slide 9: Verification of TL models
Directed functional testing
RTL Co-Simulation
DUT (SystemC)
DUT (SystemC)
Refer.(VHDL)
TB (SystemC)
stimgen monitor automatic checks
signals
TL blocking transport (LT)
TL non-blocking transport (AT)
TL nb (AT)
RTL Transactor
model_lt.test
model_at.test
model_rtl.test
(core functionality only)
Test coverage: ~90% Timing accuracy (AT)*: ~90%
*with respect to available RTL tests
Notes: The models and the protocol have been verified using directed functional testing and RTL co-simulation.
For each of our models we basically have one or multiple test bench modules consisting of a stimulus generator, monitor and automatic checks.
The same test bench can be bound to the TLM model in LT mode, in AT mode and to the RTL reference model from GRLIB.
The functional coverage of the TL tests is also around 90%.
For co-simulation we use RTL transactors that have been put in place particularly for testing.
Main purpose here was to get the timing right. For the core-functionality of the models we measured an accuracy of 90 percent.

## Slide 10: What we are doing with our students in the lab:
Reordering of scrambled images received from Satellite
Solution using software shuffling (on LEON ISS)
Development of “shuffle” hardware accellerator
Working with SoCRocket and RTEMS
Notes: That’s it with part one. I will now hand over to my colleague Rolf,
who will show you what we are doing with our students in the SoCRocket lab
and a little more.
Thank you very much.